## Slide 1: The Very Large Area gamma-ray Space Telescope (VLAST)
Guo, Jianhua (郭建华)
(jhguo@pmo.ac.cn)
Purple Mountain Observatory, CAS
(on behalf the collaboration)
Dec 18th, 2025, Nanjing
International Workshop on Cosmic Ray Direct Detection and Physics

## Slide 2: Outline
Scientific Objectives
Detector design
R & D progress
Summary

## Slide 3: MeV – TeV gamma-ray detection
There are fantastic scientific opportunities on dark matter detection, cosmic ray physics, origination of elements above Iron and time-domain & multi-messenger astronomy, via precise gamma-ray observations in a wide energy range from MeV to TeV.

## Slide 4: Dark matter indirect detection
Shen, Xia & Fan 2021
line-like?
Dark matter may annihilate or decay to gamma-ray lines. A new detector with sensitivity over 10 times more than current detectors could validate or discover line candidates, leading the research on gamma-ray-based dark matter indirect detection.

## Slide 5: Implications from DAMPE
The best potential signal of dark matter in space detection
DAMPE is much smaller than Fermi-LAT (1/10), but much better energy resolution
Similar sensitivity with Fermi-LAT, and even better in lower energies
Sci. Bull. 67, 679 (2022)
DAMPE 5yr vs Fermi-LAT 5.8yr

## Slide 6: Cosmic ray origination
Fermi collaboration (2013 Science)
bump
The bump can validate the hadronic cosmic ray sources
3D distribution of cosmic rays can be obtained by high-precision gamma-ray observations
Reveal the origin, acceleration and propagation of cosmic rays

## Slide 7: Elements above Iron
kilonova by NS mergers
MeV emission from neutron star merger / kilonova
Direct observation by a new high-sensitivity gamma-ray detector
Discovery of the source of elements above Iron in the Universe

## Slide 8: Time-domain astronomy
GeV emission from electromagnetic counterparts of GWs
GeV emission from TDE
Monitoring the GeV emissions/bursts
Revealing new mechanisms of NS merger, TDE, etc.

## Slide 9: Multi-messenger astronomy
LIGO (2017)
IceCube et al. (2018)

## Slide 10: VLAST
Very Large Area gamma-ray Space Telescope (VLAST), the successor of DAMPE
The first 10 m2 sr level gamma-ray satellite (~20 tons)
Leading the research on dark matter detection and time-domain astronomy based on MeV - TeV gamma-rays
Y.Z. Fan et al., Acta Astronomica Sinica 63(2022)27

## Slide 11: VLAST -- IRFs
large accepance
VLAST
Fermi-LAT
high angular resolution
high energy resolution
VLAST
Fermi-LAT
Fermi-LAT
VLAST
some space-based gamma-ray missions |  |  |  | 
facility | acceptance (m2 sr) | energy range | energy resolution (@10GeV) | angular resolution (@50GeV)
Fermi-LAT | ～2 | 20 MeV-300 GeV | ~6.0% | ~ 0.10 deg
DAMPE | ～0.2 | 5 GeV-10 TeV | ~1.5% | ~ 0.10 deg
AMS-100 (concept) | ~30 | 0.1 GeV-10 TeV |  | ~ 0.03 deg
APT | ~20 | 1 MeV-10 TeV | ～20% | ~ 0.10 deg
HERD | ~2 | 0.5 GeV-10 TeV | ~1.5% | 
VLAST | ~10 | 1 MeV-10 TeV | ~1.5% | ～0.10 deg

## Slide 12: Observation mode
sky survey
Design of observation modes
sky survey：full sky survey in two orbits
pointing mode：specific points/regions
opportunity mode
Transient source：rely on Beidou communications within 120s
1 month exposure

## Slide 13: Outline
Scientific Objectives
Detector design
R & D progress
Summary

## Slide 14: Design of VLAST
Compton
event
Pair
event
Y.Z. Fan et al., Acta Astronomica Sinica 63(2022)27
Major payloads:
ACD (Anti Coincidence Detector)
STED (Silicon Tracker and low Energy gamma-ray Detector)
HEIC (High Energy Imaging Calorimeter)
2×2 matrix
each unit: 1.2×1.2 m2
Weight: ~1.6 tons in total

## Slide 15: Anti-Coindicence Detector
structure
unit
Major functions
  distinguish electron/gamma
  measuring charge for light nuclei
Major technical indices
  unit size：<1000cm2
  charge range：electron, nuclei (Z=1~8)
  efficiency：better than 99.97%
  trigger signal for charged particles
  10 kHz/m2
Detector
  top: 3100mm×3100 mm
  side:3100mm× 600 mm
  unit size: 300mm×300 mm
  readout: WLSF
electronics
  PMT (or SiPM) +charge ASIC

## Slide 16: Silicon Tracker and low Energy gamma-ray Detector
Major functions
  GeV- TeV: track measurement for pair converted electrons
  MeV: direction and energy
Major technical indices
  layers：8 superlayers (one CsI layer + two silicon layers)
  area：>= 2800mm×2800 mm；
  energy range：1-100 MeV
  angular resolution <0.1°@50GeV
Detector + electronics
  CsI+WLSF，SiPM+waveshape
  inheriting current techniques of silicon microstrip tracker at DAMPE
  exploring the fiber substitute for silicon microstrip
scintillator fiber
CsI layer + silicon tracker layer

## Slide 17: High Energy Imaging Calorimeter
Major functions
  energy measurement
  proton/electron discrimination
  trigger
Major technical indices
  area：~2400mm×2400 mm
  energy range：0.1GeV~20TeV (gamma)
  energy resolution: <2%@50GeV
  proton rejection: >104@50GeV
  trigger threshold：<0.5MIPs
Detector + electronics
  3D pixels：~3cm cubes, 1 layer
  long bars：1200×25×25 mm3，4 layers (X+Y)， 2×2 matrix
  multi-gain readouts
structure
bar readout

## Slide 18: Payload Data Manager
Major functions
  trigger and DAQ
  on-orbit multi-level trigger algorithm, reducing the event rate
Major technical indices
  event rate：2kHz on average
  data storage：64GB per day？
Trigger approach
  MeV gamma: CsI independent
  GeV gamma: ACD + STED + HEIC
  >5GeV: HEIC only

## Slide 19: Outline
Scientific Objectives
Detector design
R & D progress
Summary

## Slide 20: Anti-Coindicence Detector
ACD
unit product: done
unit test: efficiency >99.99%
first prototype: done

## Slide 21: Silicon Tracker and low Energy gamma-ray Detector
CsI readout
crystal: done
fiber: cut and polish done
first module: done
silicon tracker
module: 40cm and 70cm
first prototype: 11 ladders, done

## Slide 22: High Energy Imaging Calorimeter
3D pixels
design done
pixel: 30mm*30mm*30mm
first prototype: 4 layers, done
long bar
electronics: done
first prototype：5 layers, done

## Slide 23: Beam Test in the past two years
Beam Test at CERN：
  2023: Week37, PS-T9 (e-/p)
  2023: Week40, SPS-H8 (ions)
  2024: Week20, SPS-H2 (e-/pi-)
  2024: Week21-22, PS-T9 (e-/p/γ)
  2024: Week46, SPS-H4(ions)
  status for prototype：
  ACD (pile + long strip)
  STED (Silicon + CsI)
  HEIC (3D pixel + long bar)
BT@CERN-PS

## Slide 24: Beam Test in the past two years
BT@CERN-SPS
some preliminary results

## Slide 25: Pathfinder (VLAST-P)
Specification | 
Field of View | ±45°
Energy range | 50MeV~5GeV
Energy Resolution（Sigma） | <10%@(200MeV~1GeV)
Acceptance | > 100cm2 Sr @100MeV
ACD Efficiency for MIPs | > 99.9%
Spatial resolution (Sigma) | <50um
Mass | ~178Kg
Technical purpose：
  ACD detector developed by IMP
  Silicon-strip detector developed by PMO
  ECAL developed by USTC
Scientific purpose:
  Observing high-energy radiation processes during solar flares, studying the radiation mechanisms of solar flares
  Observing other high-energy gamma-ray bursts beyond the Sun

## Slide 26: Pathfinder (VLAST-P)
ACD
ECAL
Tracker
VLAST-p
Electronics Model：
  Assembled in May
  Thermal cycle test, mechanics test and thermal vacuum test by June
  Flight Model：
  Will finish assembly by the end of next Feb.
  Plan to be launched by the end of 2026

## Slide 27: Summary/Overview
A flagship for space-based gamma-ray detection：Very Large Area gamma-ray Space Telescope（VLAST）
Leading the researches on gamma-ray-based dark matter indirect detection and time-domain astronomy
Scientific objectives：
Indirect detection of dark matter (DM) particles
  1) GeV emission by DM annihilation/decay from regions like dwarf spheroidal galaxies
  2) Line-like structure by DM annihilation/decay
  3) Axions or axion-like particles
  4) DM signals in cosmic ray electrons
Gamma-ray astronomy
  1) Electromagnetic counterparts of gravitational waves, neutrinos and tidal disruption events
  2) New GeV bursting or high-z sources
  3) Measuring the GeV gamma-ray horizon of the Universe
Cosmic ray physics
  1) Nearby electron sources
  2) New spectral structures in high-energy range
Major payloads:
ACD (Anti Coincidence Detector)
STED (Silicon Tracker and low Energy gamma-ray Detector)
HEIC (High Energy Imaging Calorimeter)
An prototype has been sent to CERN for Beam Test in the past two years (2023-2034)
Handle the key techniques in a few years
A pathfinder project has been established and will be launched in 2026

## Slide 28: Summary/Overview
A flagship for space-based gamma-ray detection：Very Large Area gamma-ray Space Telescope（VLAST）
Leading the researches on gamma-ray-based dark matter indirect detection and time-domain astronomy
Scientific objectives：
Indirect detection of dark matter (DM) particles
  1) GeV emission by DM annihilation/decay from regions like dwarf spheroidal galaxies
  2) Line-like structure by DM annihilation/decay
  3) Axions or axion-like particles
  4) DM signals in cosmic ray electrons
Gamma-ray astronomy
  1) Electromagnetic counterparts of gravitational waves, neutrinos and tidal disruption events
  2) New GeV bursting or high-z sources
  3) Measuring the GeV gamma-ray horizon of the Universe
Cosmic ray physics
  1) Nearby electron sources
  2) New spectral structures in high-energy range
Major payloads:
ACD (Anti Coincidence Detector)
STED (Silicon Tracker and low Energy gamma-ray Detector)
HEIC (High Energy Imaging Calorimeter)
An prototype has been sent to CERN for Beam Test in the past two years (2023-2034)
Handle the key techniques in a few years
A pathfinder project has been established and will be launched in 2026
Thank you for your attention!